## Slide 1: MULTICYCLE PROCESSOR

## Slide 2: Muticycle Processor
A single-cycle processor is simple to implement. However, it has multiple disadvantages, such as the cycle time being limited by the longest instruction, which is the load word (lw) instruction.
The multicycle processor solves these problems, providing higher clock speed, different instructions which use different numbers of steps (thus simpler instructions complete faster), and utilization of only one adder, which is reused for different purposes throughout the entire cycle.

## Slide 3: Multicycle vs. Single Cycle

## Slide 4: Complete Multicycle MIPS Processor

## Slide 5: ALU

## Slide 6: ALU
The Arithmetic logic unit is a combinational circuit that performs arithmetic and bitwise operations on integer binary numbers. It is mainly composed of two input operands, a function selector, output result and flag bits. In this multicycle processor design, zero flag is used and passed to the control unit.

## Slide 8: Code for ALU
module alu( input [31:0] A, B,
input [2:0] F,
output reg [31:0] Y,
output Zero);
always @ ( * )
case (F[2:0])
3'b000: Y <= A & B; // AND
3'b001: Y <= A | B; // OR
3'b010: Y <= A + B; // ADD
//3'b011: Y <= 0; // not used
3'b110: Y <= A - B; // SUB
3'b111: Y <= A < B ? 1:0; //SLT
default: Y <= 0; //default to 0, should not happen
endcase
assign Zero = (Y == 32'b0);
endmodule

## Slide 9: Testbench for ALU
module alu_t();
reg [31:0] A, B;
reg [2:0] F;
wire Zero;
wire [31:0] Y;
alu uut (A, B, F, Y, Zero);
initial begin
A = 0;
B = 0;
F = 0;
#8 A = 2; B = 3;
#8 A = 5; B = 7;
#8 A = 13; B = 10;
#8 A = 25; B = 25;
#8 A = 35; B = 56;
#8 A = 75; B = 100;
#8 A = 200; B = 155;
#8 A = 360; B = 400;
#8 A = 1023; B = 780;
#8 A = 1570; B = 2047;
end
always
begin
#1 F = F + 1;
end
endmodule

## Slide 10: Waveform of the ALU

## Slide 11: MEMORY

## Slide 12: What is a Memory?
Memory refers to a device that is used to store information for immediate use in a computer or related computer hardware device. A single cell memory element is just a single scannable flip flop.
Scannable Flipflop

## Slide 13: Cont. Memory
A memory unit can be made by creating an array of flipflops that can be read and written. The following figure shows the basic symbol for the memory.

## Slide 14: Generic Memory Symbol
Memory Array Function
The memory size can be determined by multiplying its width and depth in this case, the memory unit above can store 12bits of data.

## Slide 15: Memory Organization
The memory can read and write data. Each block of memory has its own address that is used to locate the data. The memory is composed of inputs: clock, for timing, write enable latch, address bits for locating data, write data, the data needed to be stored. The output is only read data that outputs data based on the current address bit input.
In multicycle processor, the memory is shared. Both instruction and data share the same memory block. A single memory block is a machine code that is derived from the assembly code of the program. To interpret machine language, one must decipher the fields of each 32-bit instruction word. Different instructions use different formats, but all formats start with a 6-bit opcode field. Thus, the best place to begin is to look at the opcode. If it is 0, the instruction is R-type; otherwise it is I-type or J-type.

## Slide 19: Code for Memory
module mem(input clk, we,
input [31:0] a, wd,
output [31:0] rd);
reg [31:0] RAM[63:0];
initial begin
RAM[0] <= 32'h20020005;
RAM[1] <= 32'h2003000c;
RAM[2] <= 32'h2067fff7;
RAM[3] <= 32'h00e22025;
RAM[4] <= 32'h00642824;
RAM[5] <= 32'h00a42820;
RAM[6] <= 32'h10a7000a;
RAM[7] <= 32'h0064202a;
RAM[8] <= 32'h10800001;
RAM[9] <= 32'h20050000;
RAM[10] <= 32'h00e2202a;
RAM[11] <= 32'h00853820;
RAM[12] <= 32'h00e23822;
RAM[13] <= 32'hac670044;
RAM[14] <= 32'h8c020050;
RAM[15] <= 32'h08000011;
RAM[16] <= 32'h20020001;
RAM[17] <= 32'hac020054;
end
assign rd = RAM[a[31:2]]; // word aligned
always @(posedge clk)
if (we)
RAM[a[31:2]] <= wd;
endmodule

## Slide 20: Testbench for Memory
module mem_tb;
reg clk, we;
reg [31:0] a, wd;
wire [31:0] rd;
mem uut(clk, we, a, wd, rd);
always begin
clk <= 1; #5; clk <= 0; #5;
end
initial begin
we <= 0;
wd <= 0;
end
initial begin
a <= 10; //read memory from address 10
#10;
a <= 25; //read memory from address 25
#10;
a <= 25;
we <= 1;
wd <= 32'habcd1234; //write abcd1234 to address 25
#10;
we <= 0;
a <= 5; //read memory from address 5
#10;
a <= 25; //read memory from address 25
#10;
$stop;
end
endmodule

## Slide 21: Waveform of Memory

## Slide 22: REGISTER

## Slide 23: Register:
A register is a quick-access storage location for a processor
Usually comprises of a small amount of storage, and each of these storage parts may be either read-only or write-only
Registers are able to store light data for an amount of time, and can serve as an interface which allows the CPU to communicate with the I/O and memory components

## Slide 24: To demonstrate the flow of processes of a register, a flowchart is illustrated below:

## Slide 25: The Register Set
The MIPS architecture defines 32 registers. Each register has a name and a number ranging from 0 to 31. The following table lists the name, number, and use for each register. $0 always contains the value 0 because this constant is frequently used in computer programs.

## Slide 26: Code for Register :
module regfile (input clk,
input we3,
input [4:0] ra1, ra2, ra3,
input [31:0] wd3,
output [31:0] rd1, rd2);
reg [31:0] rf [31:0];
always @ (posedge clk)
if (we3)
rf[wa3] <= wd3;
assign rd1 = (ra1 != 0) ? rf[ra1]:0;
assign rd2 = (ra2 != 0) ? rf[ra2]:0;
endmodule
Notes: Ra1, ra2, ra3 (3 ported register files
Read two ports cominationally
Write third port on the rising edge of the clock
Register 0 hardwred to 0

## Slide 27: Testbench for Register:
`timescale 1 ns / 1 ns
module register_file_tst();
reg clk, we3;
reg [4:0] a1, a2,a3;
reg [31:0] wd3;
wire [31:0] rd1, rd2;
register_file UUT (clk, we3,a1,a2, a3,wd3, rd1, rd2);
initial begin
wd3 =32'b0;
a1 = 5'b0;
a2 = 5'b0;
a3 = 5'b0;

## Slide 28
we3 = 1'b0;
clk = 1'b0;
#100
we3=1'b1;
#20
wd3=32'habcd_efab;
a1=5'h0;
a2=5'h0;
a3=5'h1;
#20
wd3=32'h0123_4567;
a1=5'h1;
a2=5'h0;
a3=5'h2;
#20
wd3=32'hcccc_cccc;
a1=5'h2;
a2=5'h1;
a3=5'h3;
#20
wd3=32'h3333_4567;
a1=5'h2;
a2=5'h3;
a3=5'h1;
end
always begin
#10;
clk =~clk;
end
endmodule

## Slide 29: Waveform of the Register:

## Slide 30: CONTROL UNIT

## Slide 31: Control Unit
The control unit is the part of the computer’s central processing unit (CPU), which directs the operation of the processor. It was included as part of the von Neumann architecture by John von Neumann.
It is the responsibility of the control unit to tell the computer’s memory, arithmetic/logic unit (ALU), and input/output (I/O) devices how to respond to the instructions that have been sent to the processor. It fetches internal instructions of the programs from the main memory to the processor instruction register, and based on this register contents, the control unit generates a control signal that supervises the execution of these instructions.

## Slide 33: Cont. Control Unit
The controller will have two major modules, the main decoder and the ALU decoder. The controller will read inputs from the top level in which it will provide control signals as outputs which are processed by the main decoder and the ALU decoder. The main decoder uses opcodes as input while the ALU decoder uses functions as input. The alu_op output port of the main decoder will be used as an input port by the ALU decoder. A more detailed operation on how the controller works will be discussed in the state diagram.

## Slide 34: Control Unit Internal Structure

## Slide 35: Control Unit State Diagram

## Slide 36: Control Unit State Table

## Slide 37: Code for the Control Unit
// The main controller produces multiplexer select and register enable
// signals for the datapath. The select signals are MemtoReg, RegDst,
// IorD, PCSrc, ALUSrcB, and ALUSrcA. The enable signals are IRWrite,
// MemWrite, PCWrite, Branch, and RegWrite.
module controller(input clk, reset,
input [5:0] op, funct,
input zero,
output pcen, memwrite, irwrite, regwrite,
output alusrca, iord, memtoreg, regdst,
output [1:0] alusrcb, output [1:0] pcsrc,
output [2:0] alucontrol);
wire [1:0] aluop;
wire branch, pcwrite;

## Slide 38
// Main Decoder and ALU Decoder subunits.
maindec md(clk, reset, op,
pcwrite, memwrite, irwrite, regwrite,
alusrca, branch, iord, memtoreg, regdst,
alusrcb, pcsrc, aluop);
aludec
ad(funct, aluop, alucontrol);
assign pcen = pcwrite | (branch & zero);
endmodule

## Slide 39: Main Decoder
// The controller receives the current instruction from the datapath
// and tell the datapath how to execute that instruction.
module maindec(input clk, reset,
input [5:0] op,
output pcwrite, memwrite, irwrite, regwrite,
output alusrca, branch, iord, memtoreg, regdst,
output [1:0] alusrcb,
output [1:0] pcsrc,
output [1:0] aluop);

## Slide 40
// FSM States
parameter FETCH = 5'b00000; // State 0
parameter DECODE = 5'b00001; // State 1
parameter MEMADR = 5'b00010; // State 2
parameter MEMRD = 5'b00011; // State 3
parameter MEMWB = 5'b00100; // State 4
parameter MEMWR = 5'b00101; // State 5
parameter EXECUTE = 5'b00110; // State 6
parameter ALUWRITEBACK = 5'b00111; // State 7
parameter BRANCH = 5'b01000; // State 8
parameter ADDIEXECUTE = 5'b01001; // State 9
parameter ADDIWRITEBACK = 5'b01010; // state a
parameter JUMP = 5'b01011; // State b

## Slide 41
// MIPS Instruction Opcodes
parameter LW = 6'b100011; // load word lw
parameter SW = 6'b101011; // store word sw
parameter RTYPE = 6'b000000; // R-type
parameter BEQ = 6'b000100; // branch if equal beq
parameter ADDI = 6'b001000; // add immidiate addi
parameter J = 6'b000010; // jump j
reg [4:0] state, nextstate;
reg [16:0] controls;
state register
always @(posedge clk or posedge reset)
if(reset) state <= FETCH;
else state <= nextstate;

## Slide 42
// next state logic
always @( * )
case(state)
FETCH: nextstate <= DECODE;
DECODE: case(op)
LW: nextstate <= MEMADR;
SW: nextstate <= MEMADR;
RTYPE: nextstate <= EXECUTE;
BEQ: nextstate <= BRANCH;
ADDI: nextstate <= ADDIEXECUTE;
J: nextstate <= JUMP;
default: nextstate <= FETCH;
endcase
MEMADR: case(op)
LW: nextstate <= MEMRD;
SW: nextstate <= MEMWR;
default: nextstate <= FETCH;
endcase
MEMRD: nextstate <= MEMWB;
MEMWB: nextstate <= FETCH;
MEMWR: nextstate <= FETCH;
EXECUTE: nextstate <= ALUWRITEBACK;
ALUWRITEBACK: nextstate <= FETCH;
BRANCH: nextstate <= FETCH;
ADDIEXECUTE: nextstate <= ADDIWRITEBACK;
ADDIWRITEBACK: nextstate <= FETCH;
JUMP: nextstate <= FETCH;
default: nextstate <= FETCH;
endcase

## Slide 43
// output logic
assign {pcwrite, memwrite, irwrite, regwrite, alusrca, branch, iord, memtoreg, regdst, alusrcb, pcsrc, aluop} = controls;
always @( * )
case(state)
FETCH: controls <= 19'b1010_00000_0100_00;
DECODE: controls <= 19'b0000_00000_1100_00;
MEMADR: controls <= 19'b0000_10000_1000_00;
MEMRD: controls <= 19'b0000_00100_0000_00;
MEMWB: controls <= 19'b0001_00010_0000_00;
MEMWR: controls <= 19'b0100_00100_0000_00;

## Slide 44
EXECUTE: controls <= 19'b0000_10000_0000_10;
ALUWRITEBACK: controls <= 19'b0001_00001_0000_00;
BRANCH: controls <= 19'b0000_11000_0001_01;
ADDIEXECUTE: controls <= 19'b0000_10000_1000_00;
ADDIWRITEBACK: controls <= 19'b0001_00000_0000_00;
JUMP: controls <= 19'b1000_00000_0010_00;
default: controls <= 19'b0000_xxxxx_xxxx_xx; // should never happen
endcase
endmodule

## Slide 45: ALU Decoder
module aludec(input [5:0] funct,
input [1:0] aluop,
output reg [2:0] alucontrol);
always @( * )
case(aluop)
3'b000: alucontrol <= 3'b010; // add
3'b001: alucontrol <= 3'b010; // sub
// RTYPE instruction use the 6-bit funct field of instruction to specify ALU operation
3'b010: case(funct)
6'b100000: alucontrol <= 3'b010; // ADD
6'b100010: alucontrol <= 3'b110; // SUB
6'b100100: alucontrol <= 3'b000; // AND
6'b100101: alucontrol <= 3'b001; // OR
6'b101010: alucontrol <= 3'b111; // SLT
default: alucontrol <= 3'bxxx; // ???
endcase
default: alucontrol <= 3'bxxx; // ???
endcase
endmodule

## Slide 46: Testbench for Control Unit
module controllert();
reg clk, reset, zero;
reg [5:0] op, funct;
wire iord, memwrite, irwrite, regdst, memtoreg, regwrite, alusrca, pcen;
wire [1:0] alusrcb, pcsrc;
wire [2:0] alucontrol;
reg [31:0] instr;
always @ ( * ) begin
op <= instr [31:26];
funct <= instr [5:0];
end
controller uut(clk, reset, op, funct, zero, pcen, memwrite, irwrite, regwrite, alusrca, iord, memtoreg, regdst, alusrcb, pcsrc, alucontrol);
always #1 clk = ~clk;

## Slide 47
initial
begin
clk = 0;
reset = 1;
zero = 0;
#2 reset = 1; instr = 0;
#2 reset = 0; instr = 32'h20020005; //addi
#2 reset = 0; instr = 32'h20020005; //addi
#2 reset = 0; instr = 32'h20020005; //addi
#2 reset = 0; instr = 32'h20020005; //addi
#2 reset = 0; instr = 32'h2003000c; //addi
#2 reset = 0; instr = 32'h2003000c; //addi
#2 reset = 0; instr = 32'h2003000c; //addi
#2 reset = 0; instr = 32'h00e22025; //or
#2 reset = 0; instr = 32'h00e22025; //or
#2 reset = 0; instr = 32'h00e22025; //or
#2 reset = 0; instr = 32'h00e22025; //or
#2 reset = 0; instr = 32'h00642824; //and
#2 reset = 0; instr = 32'h00642824; //and
#2 reset = 0; instr = 32'h00642824; //and
#2 reset = 0; instr = 32'h00642824; //and

## Slide 48
#2 reset = 0; instr = 32'h00a42820; //add
#2 reset = 0; instr = 32'h00a42820; //add
#2 reset = 0; instr = 32'h00a42820; //add
#2 reset = 0; instr = 32'h00a42820; //add
#2 reset = 0; instr = 32'h00853820; //add
#2 reset = 0; instr = 32'h00853820; //add
#2 reset = 0; instr = 32'h00853820; //add
#2 reset = 0; instr = 32'h00853820; //add
#2 reset = 0; instr = 32'h00e23822; //sub
#2 reset = 0; instr = 32'h00e23822; //sub
#2 reset = 0; instr = 32'h00e23822; //sub
#2 reset = 0; instr = 32'h00e23822; //sub
#2 reset = 0; instr = 32'hac670044; //sw
#2 reset = 0; instr = 32'hac670044; //sw
#2 reset = 0; instr = 32'hac670044; //sw
#2 reset = 0; instr = 32'hac670044; //sw
#2 reset = 0; instr = 32'h8c020050; //lw
#2 reset = 0; instr = 32'h8c020050; //lw
#2 reset = 0; instr = 32'h8c020050; //lw
#2 reset = 0; instr = 32'h8c020050; //lw
#2 reset = 0; instr = 32'h8c020050; //lw
#2 $stop;
end

## Slide 49: Waveform of the Control Unit

## Slide 50: DATAPATH

## Slide 51: Multicycle Datapath
The design for the datapath of a MIPS processor is similar to that of the single-cycle processor, only it involves using a combined memory for both data and instructions, since by doing this it is easier to read in one cycle and is more practical. Reading or writing the data takes place in a separate cycle.

## Slide 52: Step 1: Fetch instruction from memory

## Slide 53: Step 2a: Read source operand from register file

## Slide 54: Step2b: Sign-extend the immediate

## Slide 55: Step 3: Add base address to offset

## Slide 56: Step 4: Load data from memory

## Slide 57: Step 5: Write data back to register file

## Slide 58: Step 6: Increment PC by 4

## Slide 59: Enhanced datapath for sw instruction
This completes the datapath for the lw instruction. Next, let us extend the datapath to also handle the sw instruction. Like the lw instruction, the sw instruction reads a base address from port 1 of the register file and sign-extends the immediate. The ALU adds the base address to the immediate to find the memory address. All of these functions are already supported by existing hardware in the datapath.

## Slide 60: Enhanced datapath for sw instruction

## Slide 61: Enhanced datapath for R-type instructions
For R-type instructions, the instruction is again fetched, and the two source registers are read from the register file. ALUSrcB1:0, the control input of the SrcB multiplexer, is used to choose register B as the second source register for the ALU.

## Slide 62: Enhanced datapath for R-type instructions

## Slide 63: Enhanced datapath for beq instruction
For the beq instruction, the instruction is fetched again, and the two source registers are read from the register file. To determine whether the registers are equal, the ALU subtracts the registers and, upon a zero result, sets the Zero flag. Meanwhile, the datapath must compute the next value of the PC if the branch is taken: PC′ = PC + 4 + SignImm × 4.

## Slide 64: Enhanced datapath for beq instruction

## Slide 65: Generic Building Blocks
This section contains generic building blocks that may be useful in any MIPS microarchitecture, including a left shift unit, sign-extension unit, resettable flip-flop, and multiplexer.

## Slide 66: Left Shift Unit (Multiply by 4)
Left shifters move bits and multiply by powers of 2. As the name implies, a left shifter shifts a binary number left by a specified number of positions.
Ex: 11001 LSR 2 = 00110; 11001 LSL 2 = 00100
Shifts the number to the left (LSL) and fills empty spots with 0’s.

## Slide 67: Code for Left Shift Unit
module sl2(input [31:0] a, output [31:0] y);
assign y = {a[29:0], 2'b00}; // shift left by 2
endmodule

## Slide 68: Testbench for Left Shift Unit
`timescale 1ps/1ps
module s12_tb;
reg[31:0] a;
wire[31:0] y;
initial begin
a = 32'hffffffff;
#1 a = 32'habcd1234;
#1 $stop;
end
sl2 uut(a, y);
endmodule

## Slide 69: Waveform For Left Shift Unit

## Slide 70: Sign Extension
Sign extension is the operation, in computer arithmetic, of increasing the number of bits of a binary number while preserving the number's sign (positive/negative) and value. This is done by appending digits to the most significant side of the number, following a procedure dependent on the particular signed number representation used. For example, if six bits are used to represent the number "00 1010" (decimal positive 10) and the sign extend operation increases the word length to 16 bits, then the new representation is simply "0000 0000 0000 1010". Thus, both the value and the fact that the value was positive are maintained. If ten bits are used to represent the value "11 1111 0001" (decimal negative 15) using two's complement, and this is sign extended to 16 bits, the new representation is "1111 1111 1111 0001". Thus, by padding the left side with ones, the negative sign and the value of the original number are maintained.

## Slide 71: Code for Sign Extension
module signext(input [15:0] a, output [31:0] y);
assign y = {{16{a[15]}}, a};
endmodule

## Slide 72: Testbench For Sign Extension
`timescale 1ps/1ps
module signext_tb;
reg[15:0] a;
wire[31:0] y;
initial begin
a = 32'hfff3;
#1 a = 32'h004f;
#1 $stop;
end
signext uut(a, y);
endmodule

## Slide 73: Waveform for Sign Extension

## Slide 74: Multiplexer
Multiplexers are among the most commonly used combinational circuits. They choose an output from among several possible inputs based on the value of a select signal. A multiplexer is sometimes affectionately called a mux.

## Slide 75: 2:1 multiplexer symbol and truth table

## Slide 76: Wider Multiplexers
A 4:1 multiplexer has four data inputs and one output. Two select signals are needed to choose among the four data inputs. The 4:1 multiplexer can be built using sum-of-products logic, tristates, or multiple 2:1 multiplexers.

## Slide 77: 4:1 Multiplexer

## Slide 78: 4:1 multiplexer implementations
(a) two-level logic, (b) tristates, (c) hierarchical

## Slide 79: Code for Multiplexer 2:1
module mux2 #(parameter WIDTH = 8)
(input [WIDTH-1:0] d0, d1,
input s,
output [WIDTH-1:0] y);
assign y = s ? d1 : d0;
endmodule

## Slide 80: Testbench for 2:1 Multiplexer
`timescale 1ps/1ps
module mux2_tb;
parameter WIDTH = 32;
reg [WIDTH-1:0] d0, d1;
reg s;
wire [WIDTH-1:0] y;
initial begin
d0 = 32'h1234abcd;
d1 = 32'habcd1234;
s = 0;
#2 $stop;
end
always #1 s = s + 1;
mux2 #(WIDTH) uut(d0, d1, s, y);
endmodule

## Slide 81: Waveform for 2:1 Multiplexer

## Slide 82: Code for Multiplexer 3:1
module mux3 #(parameter WIDTH = 8)
(input [WIDTH-1:0] d0, d1, d2,
input [1:0] s,
output [WIDTH-1:0] y);
assign #1 y = s[1] ? d2 : (s[0] ? d1 : d0);
endmodule

## Slide 83: Testbench for 3:1 Multiplexer
`timescale 1ps/1ps
module mux3_tb;
parameter WIDTH = 32;
reg [WIDTH-1:0] d0, d1, d2;
reg [1:0]s;
wire [WIDTH-1:0] y;
initial begin
d0 = 32'h1234abcd;
d1 = 32'habcd1234;
d2 = 32'h11112222;
s = 0;
#4 $stop;
end
always #1 s = s + 1;
mux3 #(WIDTH) uut(d0, d1, d2, s, y);
endmodule

## Slide 84: Waveform for 3:1 Multiplexer

## Slide 85: Code for Multiplexer 4:1
module mux4 #(parameter WIDTH = 8)
(input [WIDTH-1:0] d0, d1, d2, d3,
input [1:0] s,
output reg [WIDTH-1:0] y);
always @( * )
case(s)
2'b00: y <= d0;
2'b01: y <= d1;
2'b10: y <= d2;
2'b11: y <= d3;
endcase
endmodule

## Slide 86: Testbench for 4:1 Multiplexer
`timescale 1ps/1ps
module mux4_tb;
parameter WIDTH = 32;
reg [WIDTH-1:0] d0, d1, d2, d3;
reg [2:0] s;
wire [WIDTH-1:0] y;
initial begin
d0 = 32'h1234abcd;
d1 = 32'habcd1234;
d2 = 32'h11112222;
d3 = 32'h0;
s = 0;
#4 $stop;
end
always #1 s = s + 1;
mux4 #(WIDTH) uut(d0, d1, d2, d3, s, y);
endmodule

## Slide 87: Waveform for 4:1 Multiplexer

## Slide 88: Flipflop
A resettable flip-flop adds another input called RESET. When RESET is FALSE, the resettable flip-flop behaves like an ordinary D flip-flop. When RESET is TRUE, the resettable flip-flop ignores D and resets the output to 0. Resettable flip-flops are useful when we want to force a known state (i.e., 0) into all the flip-flops in a system when we first turn it on. Such flip-flops may be synchronously or asynchronously resettable. Synchronously resettable flip-flops reset themselves only on the rising edge of CLK. Asynchronously resettable flip-flops reset themselves as soon as RESET becomes TRUE, independent of CLK.

## Slide 89: Symbol for the resettable flip-flop

## Slide 90: Resettable Flip Flop with Enable
This type of flop register is similar to the simple flop register but requires enable input to be high to work.

## Slide 91: Symbol for resettable flip-flop with enable

## Slide 92: Code for Resettable Flipflop
module flopr #(parameter WIDTH = 8)
(input clk, reset,
input [WIDTH-1:0] d,
output reg [WIDTH-1:0] q);
always @(posedge clk, posedge reset)
if (reset) q <= 0;
else q <= d;
endmodule

## Slide 93: Testbench for Resettable Flipflop
`timescale 1ps/1ps
module flopr_tb;
parameter WIDTH = 32;
reg clk, reset;
reg [WIDTH-1:0] d;
wire [WIDTH-1:0] q;
always begin
clk <= 1; #1; clk <= 0; #1;
end
initial begin
d = 32'hABCD1234;
reset = 0;
#2;
d = 32'h200500C;
#2;
reset = 1;
#2;
reset = 0;
#2 $stop;
end
flopr #(WIDTH) uut(clk, reset, d, q);
endmodule

## Slide 94: Waveform for Resettable Flipflop

## Slide 95: Code for Resettable Flipflop with Enable
module flopenr #(parameter WIDTH = 8)
(input clk, reset,
input en,
input [WIDTH-1:0] d,
output reg [WIDTH-1:0] q);
always @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (en) q <= d;
endmodule

## Slide 96: Testbench for Resettable Flipflop with Enable
`timescale 1ps/1ps
module floprenr_tb;
parameter WIDTH = 32;
reg clk, reset, en;
reg [WIDTH-1:0] d;
wire [WIDTH-1:0] q;
always begin
clk <= 1; #1; clk <= 0; #1;
end
initial begin
d = 32'hABCD1234;
reset = 0;
en = 1;
#2;
d = 32'h200500C;
#2;
reset = 1;
#2;
reset = 0;
en = 0;
#2 $stop;
end
flopenr #(WIDTH) uut(clk, reset, en, d, q);
endmodule

## Slide 97: Waveform for Resettable Flipflop with Enable

## Slide 98: Completed Datapath for Multicycle Processor

## Slide 99: Code for Datapath
module datapath(input clk, reset,
input pcen, irwrite, regwrite,
input alusrca, iord, memtoreg, regdst,
input [1:0] alusrcb,
input [1:0] pcsrc,
input [2:0] alucontrol,
output [5:0] op, funct,
output zero,
output [31:0] adr, writedata,
input [31:0] readdata);
// Internal signals of the datapath module
wire [4:0] writereg;
wire [31:0] pcnext, pc;
wire [31:0] instr, data, srca, srcb;
wire [31:0] a;
wire [31:0] aluresult, aluout;
wire [31:0] signimm; // the sign-extended immediate
wire [31:0] signimmsh; // the sign-extended immediate shifted left by 2
wire [31:0] wd3, rd1, rd2;

## Slide 100
// op and funct fields to controller
assign op = instr[31:26];
assign funct = instr[5:0];
// datapath
flopenr #(32) pcreg(clk, reset, pcen, pcnext, pc);
mux2 #(32) adrmux(pc, aluout, iord, adr);
flopenr #(32) instrreg(clk, reset, irwrite, readdata, instr);
flopr #(32) datareg(clk, reset, readdata, data);
mux2 #(5) regdstmux(instr[20:16], instr[15:11], regdst, writereg);
mux2 #(32) wdmux(aluout, data, memtoreg, wd3);
regfile rf(clk, regwrite, instr[25:21], instr[20:16],
writereg, wd3, rd1, rd2);
signext se(instr[15:0], signimm);
sl2 immsh(signimm, signimmsh);

## Slide 101
flopr #(32) areg(clk, reset, rd1, a);
flopr #(32) breg(clk, reset, rd2, writedata);
mux2 #(32) srcamux(pc, a, alusrca, srca);
mux4 #(32) srcbmux(writedata, 32'b100, signimm, signimmsh,
alusrcb, srcb);
alu alu(srca, srcb, alucontrol, aluresult, zero);
flopr #(32) alureg(clk, reset, aluresult, aluout);
mux3 #(32) pcmux(aluresult, aluout,
{pc[31:28], instr[25:0], 2'b00}, pcsrc, pcnext);
endmodule

## Slide 102: Interfacing the Components

## Slide 103: Multicycle MIPS processor
// Multicycle MIPS processor
module mips(input clk, reset,
output [31:0] adr, writedata,
output memwrite,
input [31:0] readdata);
wire zero, pcen, irwrite, regwrite,
alusrca, iord, memtoreg, regdst;
wire [1:0] alusrcb;
wire [1:0] pcsrc;
wire [2:0] alucontrol;
wire [5:0] op, funct;

## Slide 104
// The control unit receives the current instruction from the datapath and tells the
// datapath how to execute that instruction.
controller c(clk, reset, op, funct, zero,
pcen, memwrite, irwrite, regwrite,
alusrca, iord, memtoreg, regdst,
alusrcb, pcsrc, alucontrol);
// The datapath operates on words of data. It
// contains structures such as memories, registers, ALUs, and multiplexers.
// MIPS is a 32-bit architecture, so we will use a 32-bit datapath.
datapath dp(clk, reset,
pcen, irwrite, regwrite,
alusrca, iord, memtoreg, regdst,
alusrcb, pcsrc, alucontrol,
op, funct, zero,
adr, writedata, readdata);
endmodule

## Slide 105: Connection of Processor and the Memory
module topmulti(input clk, reset,
output [31:0] writedata, adr,
output memwrite);
wire [31:0] readdata;
// instantiate processor and memory
mips mips(clk, reset, adr, writedata, memwrite, readdata);
mem mem(clk, memwrite, adr, writedata, readdata);
endmodule

## Slide 107: Testing and Evaluation

## Slide 108: TESTING & EVALUATION
The following tests were made first on each component to see if each one works, and then they were all tested as a top-level multi-cycle processor in order to verify that the entire program works correctly as expected.

## Slide 109: Top Level
To test the correctness of the entire multicycle processor, the following assembly code is used.

## Slide 110: MIPS Assembly Code

## Slide 111: MIPS Assembly Code
All instructions add, sub, and, or, slt, addi, lw, sw, beq, j are used in the program. If successful, it should write the value 7 to address 84D (44H)
Recall that memory is initialized with the equivalent machine code to run the program. The machine code holds both instruction and data and are decoded by the control unit and the register file.

## Slide 112: Testbench code for Multicycle Processor
module testbench();
reg clk;
reg reset;
wire [31:0] writedata, dataadr;
wire memwrite;
// keep track of execution status
reg [31:0] cycle;
// instantiate device to be tested
topmulti dut(clk, reset, writedata, dataadr, memwrite);
// initialize test
initial
begin
reset <= 1; # 12; reset <= 0;
cycle <= 1;
end

## Slide 113
// generate clock to sequence tests
always
begin
clk <= 1; # 5; clk <= 0; # 5;
cycle <= cycle + 1;
end
// check results
// If successful, it should write the value 7 to address 84
always@(negedge clk)
begin
if (memwrite) begin
if (dataadr === 84 & writedata == 7) begin
$display("Simulation succeeded");
$stop;
end else if (dataadr !== 80) begin
$display("Simulation failed");
$stop;
end
end
end
endmodule

## Slide 114: Actual Waveform of ALU using MIPS Assembly Code:
The program starts at cycle 2 after reset. The ALU arithmetic operation usually runs at ADDIEXEC and EXEC state. The cycle location of the ALU will be shown in the instruction trace. The ALU also used to increment the program counter by 4 at the FETCH state and then go to DECODE state which is iterative before and after instruction the result of the ALU is ignored at this state.

## Slide 115: initialized $2 = 5 at 30ps, initialized $3 = 12 at 70ps.

## Slide 116: initialized $7 = $3 - 9 = 12 - 9 = 3 at 110ps. $4 <= 3 or 5 = 7 at 150ps.

## Slide 117: $5 <= 12 and 7 = 4 at 190ps, $5 = 4 + 7 = 11 at 230ps

## Slide 118: $4 = 12 < 7 = 0, zero = 1 at 300ps

## Slide 119: $4 = 3 < 5 = 1 at 370ps

## Slide 120: $7 = 1 + 11 = 12 at 410ps, $7 = 12 - 5 = 7 at 450ps

## Slide 121: The ALU is not used for after 450ps so we don’t need the output from here.

## Slide 123: Actual Waveform of Memory using MIPS Assembly Code:
This part is just reading instruction and data from the memory at the given address until at 480ps where I-type instruction (sw, lw) is used.

## Slide 127
At 500ps the actual writing of data happens at MEMWRITE state where 7 is stored at address [50h] or [80d] at 540ps the data at [80d] is read and the 7 value is returned.

## Slide 128: At last the value 7 is stored at address [54h] or [84d] at 620ps

## Slide 129: Actual Waveform of Control Unit using MIPS Assembly Code:
The control unit outputs correctly based on the state diagram.

## Slide 136: Actual Waveform of Register File using MIPS Assembly Code:
The data is stored at the WRITEBACK state of the processor.

## Slide 137: $2 = 5 at 40ps

## Slide 138: $3 = 12 at 80ps

## Slide 139: $7 = 3 at 120ps

## Slide 140: $4 = 7 at 160ps

## Slide 141: $5 = 4 at 200ps

## Slide 142: $5 = 11 at 240ps

## Slide 143: $4 = 0 at 310ps

## Slide 145: $4 = 1 at 380ps

## Slide 146: $7 = 12 at 420ps

## Slide 147: $7 = 7 at 460ps

## Slide 149: $2 = 7 at 550ps

## Slide 150: Register is not used in the following part

## Slide 151: Actual Waveform of Datapath using MIPS Assembly Code:
The datapath elements is just the same as the ALU, memory and control unit except the program counter that handles the program flow and the signimm and signimmsh which sign extend the data.

## Slide 167: At this point, the data input is red indicating that the next memory address contains no instruction or data which is the end of the program.

## Slide 168: Actual Instruction Trace Waveform
The following waveform contains the instruction trace of the multicycle processor, the cycle, reset, program counter, instruction, state, the ALU inputs and result, zero flag and the FSM control word.

## Slide 184: At this point, the data input is red indicating that the next memory address contains no instruction or data which is the end of the program.

## Slide 185: Instruction Trace
The instruction trace contains the total cycle took for the program, the cycle count of each instruction. The ALU, FSM State and the control word. ALUResult values that are used for decoding is marked as X because it is not needed.

## Slide 186: Completed Instruction Trace Table

## Slide 191: Conclusion

## Slide 192: Conclusion
The test program took 62 cycles / 620ps to finish and the desired output is achieved. However some anomalies are found in the ALU.
The other components performs correctly as expected and no major issues are found in the processor.

## Slide 193
The zero flag outputs x value instead of zero because the scrB contains no data at the start. Where in the expected instruction trace zero = 0 at this point. This event does not cause any major faults.

## Slide 194
And at 380ps, data glitch are found. The possible cause is the A and F changes value at the same time where in practical it is not when A = 3, B = 5 and F = SLT (7), and A < B results in Y = 1 and then at a split picosecond the A changes value to 2C where A < B became false and causes Y = 1 and zero = 1 at that moment and then changing the F selector to ADD (2) resulting zero = 0. The propagation delay difference between A and F is the main reason of this.

## Slide 195: Recommendation
It is highly recommended that the code be optimized to be as short as possible, i.e. the code must be shortened for readability. It is also recommended that the variables used in the code must be uniformed and that all members assigned to work on the processor are informed clearly of the variables in order to avoid mistakes in declaring or assigning values to nonexistent variables.

## Slide 196: ASSESSMENT
The making of the entire multicycle processor in Verilog took approximately a total of 30 hours, including testing, debugging, and evaluation. Some problems encountered during the making of the program in Verilog include: At times, the ‘begin’ and ‘end’ statements may be misused, which can lead to errors similar to in languages like C, when the opening and closing braces (‘{‘ and ‘}’) are missing or misplaced. Naming conventions are also a problem; when another user creates and adds some lines of code to the program, s/he may confuse or mistake the names of the variables, creating bugs in the code. Regs and wires are also often confused, leading to testbench errors. Despite overlooking some of the errors in the program, the project was accomplished with a significant amount of knowledge acquired from the subject.
Overall, project successfully increased students' knowledge of processors, processor design, and Verilog implementation of the design. The students also further learned the importance of planning, teamwork, and effective documentation of results.